## Slide 1: Introduction to the application of the principles to Hazard Analysis and Critical Control Points (HACCP)

## Slide 2: Introduction 1
It is a scientific system of identifying hazards in food production and implementing control measures to prevent, eliminate or reduce them to acceptable levels at all stages in the food chain.
It is a food safety concept developed for NASA in the 1960s to ensure that food provided for astronauts would not cause illness.
It is the disciplined application of science to specific food process to ensure food safety

## Slide 3: Introduction 2
The CODEX Alimentarius Commission (CODEX) develops international food safety standards.
CODEX is the joint commission of the FAO and the WHO both of the UN developed the CODEX Alimentarius which is the globally accepted food standards.
The CODEX committee drafted the HACCP principles in June `1991 which was accepted in October of the same year.
Notes: CODEX is Latin for food law or code

## Slide 4: Concept
HACCP enables the food handler to do a ‘self-check’ aimed at ensuring food safety through;
  the identification of critical stages of the food preparation chain
  establishment of acceptable limits for key parameters responsible for food safety at these stages
  monitoring of the process at these critical stages to ensure that the acceptable limits are not exceeded
  establishment of actions to be taken if monitoring indicates that the acceptable limits are exceeded

## Slide 5: Why use HACCP?
Management of product safety
Reduce the increasing incidence of food safety issues
Customer Pressure - demanding safe food
Legislative requirements - national and international levels
Foundation for the development of effective food safety management system

## Slide 6: Benefits of HACCP to the food industry (1)
The systematic approach in its application allows for the identification of all potential areas of food safety concerns in the operation.
As preventative system it allows for the control of potential food safety hazards.
Increases confidence in the product
Resources are used effectively.

## Slide 7: Benefits of HACCP to the food industry (2)
Cost effective control system
Improves food safety which allows for increased market access (customers)
Provides business liability protection (legal actions by customers, regulatory sanctions etc. are reduced)
A driver for continuous improvement

## Slide 8: The Principles of HACCP
The HACCP concept consist of seven (7) principles, vis;
  Identification of hazards
  Identification of critical control points (critical stages)
  Establishing of critical limits for each critical point
  Establishing monitoring procedures
  Establishing corrective actions
  Establishing verification procedures
  Documentation and records keeping

## Slide 9: HACCP Terminologies
Control
Control measure
Corrective action
Critical Control Point (CCP)
Critical Limit
Deviation
Flow diagram
Hazard
Monitor
Step
Verification

## Slide 10: The HACCP System and Pre-requisite Programmes (PRPs)
The HACCP system as a food safety management tool can be most effective when there are sound pre-requisite programmes (PRPs) in place.
PRPs serve as the foundation on which the HACCP system is built.
  Good PRPs make HACCP work
  Bad PRPs will make HACCP fail
  In fact, no PRPs no HACCP!

## Slide 11: Overview of PRPs (1)
1.
Environmental Hygiene
  Maintenance of sanitation at food production areas; immediate and external areas
  Maintenance of sound fabric of food production area
    Floors, doors, windows, ceiling, drains in good state of repair
    Flow of drains from high risk to low risk areas
    Sound ventilation and illumination
    Light fittings and other overhead fittings not serving as potential sources of food safety hazards
  Effective cleaning programme
  Effective waste management programme
  Effective pest control programme

## Slide 12: Overview of PRPs (2)
2. Food Hygiene and Control of Cross Contamination risk
  Selection of sound food ingredients
  Good Storage Practices in the handling of food ingredients
  Control of stock (FIFO)
  Use of approved food ingredients
  Use and control of hygienic food production equipment (utensils)-effective cleaning and maintenance
  Control of food production activities- observation of right production conditions, post-production handling etc.
  Provision and use of potable water for all production activities including cleaning. (Hygienic storage of water)

## Slide 13: Overview of PRPs (3)
3. Personal Hygiene
  Food handlers trained in food hygiene and related subjects
  Food handlers understand and observe hygiene rules
  Food handlers certified fit to handle food for public consumption; 1st before employment and repeated at least twice in one calendar year
  Food handlers provided with the following and its usage enforced
    Clean locker/changing rooms
    Clean protective clothing; footwear, overcoat, headgear etc.
    Clean toilet facilities with inputs for effective hand washing and drying
    An eating area for staff
  Control of staff behaviour and movement etc.

## Slide 14: Overview of PRPs (4)
4. Records and documentation
  Documentation of activities of food safety significance e.g.
    Specifications for ingredients and materials
    Selection criteria for suppliers of ingredients and materials
    Specifications for the handling of ingredients and materials during transit
    Ingredients and materials reception protocols
    Cleaning, pest and waste management protocols etc.
  Keeping and updating records of major food safety activities.

## Slide 15: FOOD SAFETY HAZARDS

## Slide 16: What are Food Safety Hazards?
A Food Safety Hazard has been defined as “a biological, chemical or physical agent in, or condition of, food with the potential to cause an adverse health effect”.
It must be noted that hazards will vary among food production facilities producing the same foods because of differences in:
Sources of ingredients/ materials
Production protocols
Processing equipment
Duration of production
Storage conditions
The experience, knowledge and attitude of personnel.

## Slide 17: Examples Of Biological Hazards (1)
BACTERIA (SPORE-FORMING)
Clostridium botulinum
Clostridium perfringens
Bacillus cereus
BACTERIA (NON-SPORE-FORMING)
Campylobacter spp. Staphylococcus aureus
Escherichia coli Vibrio cholerae
Listeria monocytogens Yersina enterocolitica
Salmonella spp.
Shigella (S. dysenteriae)

## Slide 18: Examples Of Biological Hazards (2)
VIRUSES
Hepatitis A and E
Norwalk virus group
Rotavirus
PROTOZOA AND PARASITES
Entamoeba latum
Giardia lamblia
Ascaris lumbricoides
Taenia solium (Tape worm)

## Slide 19: Examples Of Chemical Hazards (1)
NATURALLY OCCURRING CHEMICALS
Allergens
Mycotoxins (e.g. aflatoxin)
Scombrotoxin (Histamine)
Shellfish toxins (e.g. Paralytic shellfish poisoning-PSP)
ADDED CHEMICALS
Agricultural chemicals
Pesticides
Fertilizers
Antibiotics
Growth hormones

## Slide 20: Examples Of Chemical Hazards (2)
Prohibited substances
Direct
Indirect
Toxic elements and compounds
Lead, Zinc, Mercury, Arsenic, Cyanide
Vitamins and minerals contaminants
Lubricants, Cleaners, Sanitizers, Coatings, Paints, Pest
Control Chemicals
From Packaging materials
Plasticizers, Adhesives, Lead, Tin, Printing/coding inks

## Slide 21: Examples Of Physical Hazards (1)
MATERIAL | INJURY POTENTIAL | SOURCES
Glass | Cuts, Bleeding; | Bottles, jars, light fittings, gauge covers etc.
Wood | Cuts, infection, Choking | Field sources, Pallets, boxes, building materials
Stones | Choking, broken teeth | Fields, buildings
Metal | Cuts, infection | Machinery, fields, wire, employees

## Slide 22: Examples Of Physical Hazards (2)
MATERIAL | INJURY POTENTIAL | SOURCES
Insulation | Choking; long-term if asbestos | Building materials
Plastic | Choking, cuts, infection | Packaging, pallets, equipment
Personal effects | Choking, cuts, broken teeth | employees

## Slide 23: Examples of Control Measures
Use of cleaned and sterilized production utensils
Qualification of the supplier
Calibration of balances
Qualification of the buyer
Certification of potable water
Maintenance of the appropriate temperature
Training programmes of operatives
Disinfection and maintenance of equipment

## Slide 24: Practical Exercise 3

## Slide 25: Identification of hazards, the source and determination of measures to control them.
Principle 1****
Select a food item (e.g. Packaged water, flavoured drink).
Consider the food ingredients and materials.
Indicate the production process in a form of flow diagram (Production protocol/ Production process).
Using a table as shown below identify the possible hazards that may be associated with food item, their sources and control measures.

## Slide 26: Identification of hazards, the source and determination of measures to control them.
Process Step | Hazard | Source | Control Measure

## Slide 27: Hint - 1
Ingredients/ materials
Draw a flow diagram indicating how to produce the above item.
Conduct a hazard analysis and establish the control measures for hazards that may be identified with the food item

## Slide 28: Hint-2
Confirm if the prepared flow diagram as drawn matches what is practiced in the production room
  You may consult the supervisors etc. to confirm this
  Make all necessary corrections to the diagram and re-confirm
(The procedure is necessary so that we can conduct a very good hazard analysis in order not to miss any potential hazard that may occur along the chain)

## Slide 29: CCPs, Critical Limits and Monitoring Procedures

## Slide 30: Identification of Critical Control Points (CCPs) [Critical Stages in the food production chain ]
Principle 2
Control measures may be established for all potential hazards identified along the various stages of the food chain
Those stages along the food chain where controls are necessary to ensure the safety of the food are called the critical control points (CCPs)

## Slide 31: CCPs (1)
There may be other control points (CPs) but these may not be critical as other production processes along the line may prevent, eliminate or reduce the identified hazard to its acceptable level.
For example, hygiene of personnel replacing filters is a control measure to prevent transfer of bacteria from the personnel on to the filter. However this stage is not a critical control point as the water would be further sanitized by U. V light before packaging.

## Slide 32: CCPs (2)
The U. V sanitization step/stage is therefore the critical control point (CCP) as any bacteria contamination/survival at this stage would be transferred to the customer
CCPs are usually associated with the final stages of the food chain where no further production processes are carried out.
CCPs are usually identified using what is referred to as a “decision tree”.

## Slide 33: CCPs (3)
(A decision tree is a series of logical questions which must be answered to establish if a step is critical or not to food safety)
CCP identification may also be supported by documentation
Experience is often applied in place of the decision tree

## Slide 34: Tree Approach

## Slide 35: CCPs (4)
Types of CCP
A point, step or procedure where a hazard may be:
Prevented from happening
Prevented from getting worse
Reduced
Eliminated

## Slide 36: Establishing of critical limits for each critical point (1)
Principle 3
A criterion which separates acceptability from unacceptability.
Must be measurable by test or observation
Criteria which must be met by each control measure at a CCP
Critical Limits
Must be properly measured
May need further investigation to set, e.g.
  Expert advise
  Scientific literature.

## Slide 37: Establishing of critical limits for each critical point (2)
Critical Limits
Must be as simple and Rapid as possible
  Temperature
  Time
  pH
  Viscosity
  Brix
  Colour
  Not (Salmonella absent in 25g)

## Slide 38: Establishing of critical limits for each critical point (3)
Target Levels
Control criteria which are more stringent than Critical Limits, and which can be used to take action and reduce the risk of deviation
      Provide a buffer zone for process management
Deviated foods may be destroyed (unfit for human consumption), divert for other uses, reworked etc.
All these come with a cost to the company.

## Slide 39: Establishing monitoring procedures
Principle 4
Monitor “The act of conducting a planned sequence of observations or measurements of control parameters to assess whether a CCP is under control” (Codex 1997)
By Monitoring, the CCP deviations from the established criteria (Limit) will be detected
This allows corrective action to be taken before the process is out of control and the food has to be rejected.

## Slide 40: Monitoring of CCPs (1)
Rapid methods of Inspection are required to monitor CCPs
  Temperature measurements
  Time settings
  pH measurements
  Metal detectors
*Microbiological testing is of limited value (Why?)

## Slide 41: Monitoring of CCPs (2)
Monitoring procedures must demonstrate that the CCP is under control
  Continuous monitoring where possible
  Capable of detecting process variation before its too late
  Capable of detecting when critical limit is needed
  Containing an alarm system to ensure corrective action
    “bells and whistle’
    Frequent monitoring
    Authority to act

## Slide 42: Monitoring of CCPs (3)
Where to measure:-
At most likely point of infringement e.g.
  Cool spot in oven
  Warm spot in refrigerator
Train staff how to monitor correctly!!

## Slide 43: Corrective Action, Verification, Records and Documentation Procedures

## Slide 44: Establishing corrective action procedures to be taken when necessary
Principle 5
Corrective Action “ Any action to be taken when the results of monitoring at the CCP indicate a loss of control” (Codex 1997)
Actions must be taken immediately, when the process is heading out of control
This way a food safety hazard will be avoided.

## Slide 45: Corrective Action (1)
What to do when something goes wrong /Immediate Action:-
Who is to take the action?
What is to be done and when?
Who is to be informed?
(Do we still have the product?)

## Slide 46: Corrective Action (2)
What happens to the product?
Divert to other use
Re-work
Discard
Investigation
What caused the problem?
How can recurrence be prevented?
What corrective action has been taken?
Has the incident been recorded?

## Slide 47: Corrective Action (3)
Responsibility:-
Who assumes responsibility for decision making when corrective actions are taken?

## Slide 48: Establishing verification procedures to ensure that the HACCP system is working efficiently
Principle 6
Verification:- The application of methods, procedures, tests and other evaluations, in addition to monitoring, to determine compliance with the HACCP Plan”
Validation:- The assessment of the HACCP plan before implementation to provide confirmation that it is valid, accurate and complete
Codex:- “ Obtaining evidence that the elements of the HACCP plan are effective”

## Slide 49: Verification
Validation of the System
  Review of the HACCP system and its records
  Validation of critical Limits
  Microbiological tests
Verification confirms that a system is available and it is working
A form of assessment/audit to identify weakness in the system, if any, before it becomes a failure.
An effective HACCP system is to eliminate microbes from the food. A verification procedure to confirm this is subjecting the food product to microbiological testing.

## Slide 50: Documentation of the system and maintaining records of results
Documentation should be in the form HACCP manual
Records form objective evidence on the implementation of the system
Records are important for:
  Internal audits
  External audits
  Cases of litigation

## Slide 51: Documentation and records keeping (1)
Documents will include:-
Food ingredient and materials specification
Plan of the production facility in relation to production processes
Production flow diagram
HACCP plan
Procedures and work instructions for CCPs in HACCP plan
HACCP records

## Slide 52: Documentation and records keeping (2)
Supporting documentation
Cleaning Schedules
Training records of all personnel
Calibration records and certificates
Pest policy
Glass policy
Metal policy

## Slide 53: Documentation and records keeping (3)
HACCP Records
Critical food ingredients test records
Cooking records
Cleaning and disinfection records
Cooking deviation records
Corrective action and disposal records
Details of HACCP audits, including non-compliances and corrective actions
Process verification data

## Slide 54: Implementation of a HACCP System and Internal Audit Protocols for the Food Service Industry

## Slide 55: Guidelines for the implementation of HACCP (1)
Prior to application of HACCP there is the need to improve on existing PRPs
Management must be committed for the success of the programme
The following must be considered during hazard identification and evaluation; impact of food ingredients, role of production process to control hazard, categories of consumers of concern etc.

## Slide 56: Guidelines for the implementation of HACCP (2)
HACCP should be applied to each specific operation separately.
The HACCP application should be reviewed and necessary changes made when any modification is made in the product, production process, or any step.

## Slide 57: Logic sequence for the implementation of HACCP(1)
The implementation of the HACCP principles consists of the following tasks;
Assemble HACCP Team
Describe Food product
Identify Intended Use
Construct Flow Diagram
On-site Confirmation of Flow Diagram (Walk the production line)

## Slide 58: Logic sequence for the implementation of HACCP(2)
6. List all Potential Hazards/Conduct a Hazard
Analysis/Consider Control Measures – PRINCIPLE 1
7. Determine Critical Control Points (CCPs) – PRINCIPLE 2
8. Establish Critical Limits for each CCP –
PRINCIPLE 3
9. Establish a monitoring system for each CCP – PRINCIPLE 4

## Slide 59: Logic sequence for the implementation of HACCP(3)
10. Establish Corrective actions – PRINCIPLE 5
11. Establish Verification Procedures – PRINCIPLE 6
12. Establish Documentation and Record Keeping – PRINCIPLE 7

## Slide 60: Functions of the HACCP team (1)
Identification of Scope of the HACCP plan ; limit to food product and process type, define the type(s) of hazards to be included- biological, physical, chemical.
Other Responsibilities
Plans HACCP Project
Completes study and generates HACCP documentation

## Slide 61: Functions of the HACCP team (2)
Ensures verification of the HACCP plan
Communicates and trains
Reviews deviations from CCPs
Reviews HACCP activities in response to change
Schedules and conducts internal audits

## Slide 62: Why Use A Team? (1)
A greater diversity of knowledge, skill and experience
A greater variety of problems can be solved that are beyond the ability of any individual
Processes which cross departments can be more easily tackled
Recommendations are more likely to be accepted and implemented

## Slide 63: Why Use A Team? (2)
The approach can be encouraging to team members and boosts morale
The workload can be shared appropriately
A challenging environment can be created which questions existing practices and assumptions

## Slide 64: Planning the HACCP project
Where are we starting from?
  What are our current capabilities?
  Gap analysis
  What additional resources are required?
  How big is the task?
How should we structure the HACCP system?

## Slide 65: Problems Encountered when Introducing HACCP

## Slide 66
THANK U