## Slide 1: BIOL 252: MICROBIAL ECOLOGY 2019/2020

## Slide 2: WASTEWATER TREATMENT

## Slide 3: Where does it all go!
Where does the water from the washer go?
When you flush the toilet where does the contents go?
By gravity flow, the waste is on its way to your local wastewater treatment plant!

## Slide 4
4
NORWEGIAN UNIVERSITY OF LIFE SCIENCES
90% of the worlds wastewater does not receive any treatment
(Corcoran et al. 2010)

## Slide 5: WASTEWATER TREATMENT
Applies knowledge and technology to improve or upgrade the quality of wastewater.
To reduce organic matter content of wastewater (i.e. reduction of BOD)
Removal/reduction of nutrients (N, P) to reduce pollution of receiving surface waters or groundwater if the effluents are applied onto land
Removal or inactivation of pathogenic microbes and parasites

## Slide 6: Why treat wastewater?
Causes a demand for dissolved oxygen (lower DO levels of streams)
Adds nutrients (nitrate and phosphate) to cause excessive growth
Increases suspended solids or sediments in streams (turbidity increase)

## Slide 7
Wastewater Treatment
Tertiary

## Slide 8
Sludge disposal to sea, land burial, incineration, composting
Screening
Primary settlement
Sludge digestion
Secondary treatment activated sludge trickle
Tertiary treatment; chlorination, UV, ozone
Effluent disposal; river, sea, irrigation
Wastewater Treatment

## Slide 9: Wastewater Treatment
Conventional Sewage Treatment
  Processes
    Primary Treatment
      Mechanical process
        Screening
        Grinding
        Grit Chamber (heavy particles - “grit”)
        Sedimentation Tank/ settling tank (suspended solids - “sludge”)

## Slide 10
Conventional Sewage Treatment
  Processes
    Secondary Treatment
      Biological process
        Uses bacteria to removed Oxygen demanding wastes (ODW) and lower BOD
      Types
        Trickling Filter
        Activated Sludge

## Slide 11: Trickling filter
Is a bed of crushed rocks or molded plastics about 2m thick
The bed must be large to allow air penetrate to the bottom and with a large surface area
Wastewater (effluent) is sprayed onto it
The effluent slowly passes through the bed

## Slide 12
Biofilms in the effluent attach to the rocks and plastics
Bacteria in the biofilms extract and digest organic compounds (BOD) up to 80-85%
Protozoa and Rotifers are mainly responsible for removal of suspended solids

## Slide 13: Activated sludge system
In the aeration tank, Air or pure oxygen is passed through the effluent
Here some sludge from the OLD batch is added to the NEW incoming sewage
This inoculum is called activated sludge as it contains large numbers of sewage-metabolizing microbes (Zoogloea bacteria)
These microbes oxidizes the organic matter in the effluent into carbon dioxide and water

## Slide 14: Activated Sludge System
This produces bacteria containing masses called Floc or sludge granules
After 4 to 8 hrs the whole content is transferred to a settling tank where the floc settles out removing much of the organic matter
The solids are then treated in a sludge digester
The effluent is then discharged

## Slide 15: Sludge digestion
Generated sludge are pumped into an anaerobic sludge digesters
Carried out in large tanks without oxygen thus encouraging growth of anaerobic bacteria especially the methane-producing bacteria
The bacteria degrades organic matter to soluble substances and gases mostly methane (60-70%) and carbon dioxide (20-30%)
Methane is harvested and used as fuel for running the digester, cassava grating, corn milling, lighting and singing of animals

## Slide 16
Conventional Sewage Treatment
  Processes
    Secondary Treatment With Trickling Filters
      Effluent leaves sedimentation tank and flows through trickling filters
        Bed of stones 3-10’ deep through which sewage passes
        Bacteria gather on stones and multiply, consuming ODW
        Cleaner water trickles through pipes at bottom of filter for additional treatment

## Slide 17
Conventional Sewage Treatment
  Processes
    Secondary Treatment With Activated Sludge
      Effluent leaves sedimentation tank and is pumped to an aeration tank
      Effluent is mixed with air and sludge loaded with bacteria (“activated sludge”)
      Sludge contacts with raw sewage, and bacteria in the sludge then decompose the raw sewage, lowering BOD

## Slide 18
  Aeration and rapid mixing
Settling
collects sludge
on bottom
Secondary process
air
diffuser
From primary process
To tertiary process

## Slide 19: Rotating Biological Contactor
Series of disks several feet in diameter mounted on a shaft
The disks rotate slowly with their lower 40% submerged in wastewater
Rotation provides aeration and contact between the biofilm on the disks and the wastewater
The rotation causes the accumulated biofilm to slough off when it becomes too thick

## Slide 20
Conventional Sewage Treatment
  Processes
    Secondary Treatment With Activated Sludge
      Activated sludge-sewage mixture is called mixed liquor
      Mixed liquor leaves aeration tank and flows to another sedimentation tank where suspended solids settle out for reuse as activated sludge

## Slide 21
Conventional Sewage Treatment
  Processes
    Tertiary Treatment
      Effluent is chlorinated (kills bacteria) and released into lake, ocean or river
      Activated sludge in sedimentation tank is reused

## Slide 22: Levels of Treatment
  Primary
  removal by physical separation of grit and large objects (material to landfill for disposal)
  Secondary
  aerobic microbiological process (sludge)
  organic matter + O2  CO2 + NH3 + H2O
  NH3  NO3-
  lowers suspended solids content (into sludge)
  Tertiary
  Chlorination
aquatic nutrient
Mostly dead microbes

## Slide 23: When the treatment is done…
Effluent back to stream after
  a final carbon filtration and
  chlorination/dechlorination
Sludge – very nutrient rich
  applied directly to land as fertilizer
  incinerated (good fuel after drying)
  composted

## Slide 26: Septic tank
Areas of our country not connected to municipal sewerage systems are served by a SEPTIC TANK
Septic systems are a type of On-Site Sewage Facility
In affluent areas in Ghana, approximately 80% of the population relies on septic tanks
In Europe septic tanks are limited to rural areas only.
"septic" refers to the anaerobic bacterial environment that develops in the tank

## Slide 27: Considerations
Aerobic
Anaerobic
Biochemical/Biological Oxygen Demand
Effluent
Scum
Sludge
Sewage
Depends on two kinds of bacteria:
Aerobic
Anaerobic

## Slide 28: Treat sewage so that it is made harmless

## Slide 29
Primary treatment:
Separation of liquids and solids
Does not purify sewerage

## Slide 30: In a Septic tank….....
Here sewage enters a holding tank and suspended solids settle out
Sludge is pumped out from time to time and disposed off – Lavenda Hill
Is mostly three chambers
Effluent flows through the perforations into leaching field and decomposed by microbes

## Slide 31: Septic Tanks chamber
Sedimentation
Digestion tank
Storage of digested sludge

## Slide 33: Oxidation ponds/lagoons/stabilization ponds
Inexpensive but requires large land
Its often in TWO stages
First stage like primary treatment
Here sludge settles out in the first stage
Second stage like secondary treatment
Here it is shallow enough to allow aeration by wave action and encourage aerobic conditions for bacterial growth

## Slide 34: Oxidation ponds/lagoons/stabilization ponds
Encouraged decomposition of organic matter
Algae grows on top of the oxidation ponds,
Algae use carbon dioxide in photosynthesis to produce oxygen which promote the aerobic microbial activity

## Slide 35
Most often treated sewage is disinfected by chlorination before discharge into receiving waters (Tertiary treatment)
Sometimes it can be treated to a level of purity that allows its use as drinking water
Here a combination of UV light and other disinfectants are employed